## Slide 1
HL-69 SOIL MOISTURE SENSOR
Presented by:
Samuel Emon Halder-22101183
Pinky Akter-22101156
Presented To:
A.S. Zaforullah Momtaz
Assistant Professor
University of Asia Pacific

## Slide 2
Introduction
Senor Introduction:
The HL-69 Soil Moisture Sensor is a widely used electronic device designed to measure the moisture content of soil. It is commonly used in agriculture, gardening, and automated irrigation systems to help monitor soil conditions and optimize water usage.

## Slide 3
Working Principle
  Two Probes: Detect moisture levels by measuring conductivity.
  Analog Output: Provides variable voltage readings based on moisture content.
  Digital Output: Can be used for threshold-based automation with a comparator circuit.
  Low Power Consumption: Suitable for battery-powered applications.
  Easy Integration: Compatible with microcontrollers like Arduino and Raspberry Pi.
Key Features
Dry soil
Wet soil
Less
Conductivity
More
Conductivity
Higher Resistance
Lower Resistance
Higher Sensor Value
Lower Sensor Value
DO=High(5V)
DO=Low(0V)

## Slide 4
Connections
The sensor works on the principle of electrical resistance. When soil moisture increases, electrical conductivity improves, resulting in lower resistance and higher output voltage. Conversely, dry soil has lower conductivity, leading to higher resistance and a lower output signal.
Arduino
5V
GND
A0
Sensor
VCC
GND
A0

## Slide 5
Mechanisms
  The sensor has two probes that act as electrodes
  Higher resistance between probes when moisture is low
  Lower resistance when moisture is high
  Sensor’s comparator circuit converts analog signal into binary output
  Output remains Low for moisture signal above the threshold
  Output goes high if the moisture drops below the threshold

## Slide 6
Soil Moisture Sensor Code

## Slide 7
Applications
  Used in smart irrigation systems: Can control water supply based on soil moisture levels automatically thus reducing water wastage and optimizing irrigation.
  Precision agriculture: Helps farmers to monitor soil moisture levels and water crops adequately without overwatering.
  Landslide Prediction System: Installed in hilly areas to detect high soil moisture that could cause landslides.
  Environmental Monitoring: Can be used in measuring soil moisture in forests and wetlands. Useful for climate research purposes.

## Slide 8
THANK YOU.